100W Low Pass Filters

- The FP2 relays must be inserted into the board with the notch on the relay matching the silkscreened notch.  Install FP2 relays at the following locations:

K1

K2

K3

K4

K5

K6

K7

K8

K9

K10

K11

K12

K13

K14

- Wind 29 turns(21 inches) of 22 guage wire through each of 2 T50-2 toroids.  Install the toroids at the following locations:

L1

L2

- Wind 22 turns(17 inches) of 22 guage wire through each of 2 T50-2 toroids.  Install the toroids at the following locations:

L3

L4

- Wind 16 turns(14 inches) of 18 guage wire through each of 2 T50-2 toroids.  Install the toroids at the following locations:

L5

L6

- Wind 13 turns(12 inches) of 18 guage wire through aT50-10 toroid.  Install the toroid at the following locations:

L7

- Wind 10 turns(10 inches) of 18 guage wire through a T50-6 toroid.  Install the toroid at

L8

- Wind 11 turns(11 inches) of 18 guage wire through each of 2 T50-10 toroids.  Install the toroids at the following locations:

L9

L10

- Wind 10 turns(10 inches) of 18 guage wire through each of 2 T50-10 toroids.  Install the toroids at the following locations:

L11

L12

- Wind 8 turns(9 inches) of 18 guage wire through each of 2 T50-10 toroids.  Install the toroids at the following locations:

L13

L14

- Observing correct polarity for the diodes(align bar on diode with silkscreen bar on board) install 1N4003 diodes at the following locations:

D1

D2

D3

D4

D5

D6

D7

- Install 3.9nF capacitors at following location:

C2

- Install 2 1000pF;500V capacitors at each of the following locations:

C1

C3

- Install 1 1000pF;500V capacitor at each of the following locations:

C5

C6

C7

- Install 820pF;500V capacitors at the following locations:

C6(in parallel with the 1000 pF above)

C13

- Install 470pF;500V capacitor at the following location:

C12

C14

- Install 330pF;1KV capacitor at the following location:

C18

- Install 270pF;500V capacitor at the following location:

C22

- Install 150pF;500V capacitors at the following locations:

C17

C19

C21

C23

- Install 120pF;500V capacitors at the following locations:

C25

C27

C38

- Install 100pF;500V capacitors at the following locations:

C26 (2 in parallel)

C46

- Install 51pF;500VV capacitor at the following location:

C37

C45

C47

- Install 22pF;500pF capacitor at the following location:

C13

- Install AduM1251 I.C. At

U2

- Install PCF8574A at

U1

- Install .1uF capacitors at the following locations:

C9

C10

C28

- Install .33uF capacitor at

C30

- Install 1K resisters at the following locations:

R1

R2

R3

R4

- Install 2N7000 transistors correctly orientated at the following locations:

Q1

Q2

Q3

Q4

Q5

Q6

Q7

- Install 78L05 with correct orientation at the following location:

U3

- Install 3 X 1 Headers at the following locations:

P1

P3

P4

- Install 2 X 1 Header at

P5

- Install 4 X 1 Header at

- P6